Instructions of 380W Beam Moving Head Spot Light

Product Description:

380W Beam Moving Head is a kind of high brightness,high integration, high effect & high speed liner 3 in 1 Spot light, which combines international and domestic high quality material and advanced design and technology. This light adapts authoritative 3-phase motor, constant current circuit board & full power 600W 380V electronic ballast, 36V,24V,12V specific voltage,with exact positioning and high interference rejection. Own design optical lens leads to a high performance of beam, wash and gobo effect. The light includes one color wheel: white + 8 colors + liner CTO. 3 gobo wheel: one fixed gobo with 6 white + 9 patterns, one actional gobo with white + diaphragm + 3-phase arc actional gobo. One metal rotational gobo wheel with white + 7 removable glass patterns, stack use with effect gobo. Available for customized logo which is replaceable. Independent 8-facet and 16-facet prisms switchable for 8+16+24 beam effect. This light also includes all time liner beam zoom effect with fine adjustment ability, max beam angle 2~80 degree Light hook was designed locked on the base of light,with internal battery available for adjusting address code without electric, include RMD controller, convenient lens self-regulation function which solved stage long distance beam issue.

Specification:

Input Voltage(V): AC220V

Total Power: 600W

Fuse: 7A

Ballast: 380V Electrical Ballast

Lamp: YODN, (or other brand)

Lamp Power: 380watt

Color Temperature(CCT): 7800K

Average lifetime: 1,500 hours (pack lamp & reflection

cup to lengthen lifetime)

Motors: 15 super mute motors, XY three-phase motor

Dimmer: 0-100% linear dimming function
Color wheel: white + 8 colors

Gobo wheel: 6 white + 9 patterns

Dynamic effect gobo: white + aperture + 3 section arc dynamic effect pattern

Rotating metal gobo: white + 7 glass gobo

Prisms: 8-facet & 16-facet (can be superimposed to 24, two-way independent rotation)

Channel: 19CH

Size: 395*293*700mm (LWH)

Control mode: international standard DMX512, automatic and master/ slave mode

Surface: High temperature resistant plastic

Body color: black

IP Rating: IP20

Net Weight: 20.8kg

Before any installation, maintain and clean lamp, please make sure the power is off.

- Operation

| touch | wheel | function |
| --- | --- | --- |
| Up | turn left | option/edit |
| down | turn right | option/edit |
| OK / Enter | press the wheel | Executive start / exit |
| return | when return menu ,press the wheel | return previous page |

Set ”Modify address code” as an example, tell about the using of the touch.
1. Touch button “setting” in the main interface, and then into “setting” interface.
2. The 4 touch button in the right, are “up”, “ok”, “down”, “back”.
3. Press “up” or “down” button select “DMX address”.
4. Press “ok” button into editing state. 
5. Press “up” button or “ down” button modification address code (using the new address immediately and autosave)
6.Press “OK” button out of the editing state ( could omitted)
7. Press “back” button back to the main menu.

If using the wheel, process like bellow :  
1. In the main interface , turn the wheel, select “setting” button.
2. Press the turn wheel and then loosen, into “setting” interface.
3.In the “setting” interface,  select “DMX address”
4. Press the turn wheel and then loosen, into the editing state.
5. Turn the wheel, modification address code
6. After modification, press turn wheel and then loosen, out of the editing state.
7. Turn the wheel select “back”, press turn wheel and then loosen, back into the main interface.

- Interface description

2.1  Main Interface

Top right corner 3 button for language switching and screen rotation.

EN: English

Bottom row four button corresponding sub interface is introduced, it’s in the back.

With touch operating mode sub interface is introduced, if use wheel, corresponding relation  as follows:

Press up : turn left

Press down : turn right

Press ok : press the wheel

Use wheel operation dialog box

If ok, press the wheel. if cancel, turn the wheel.

2.2 Set up the interface

| Option | Instruction |
| --- | --- |
| Run Mode | DMX | Slave state: Accept control table or main engine |
|  | Automatic | Statistics: Automatic operation and send DMX signal for slave Note:If the bulb is putout before , the light bulb will not be full light. If you need to observe the lighting effects, please keep the light on, and then into the automatic state |
| DMX Address | 1-512 | Press OK key into edit state, its selected hundred. Press up or down,change address code.Press again OK key, selected ten editor. Press again OK key, select the edit. Press it again to exit the edit state. |
| Channel Mode | 16CH | The 17th to 20th channels are invalid. |
|  | 20CH | Control Speed of th 17th to 20th channels |
| Invert Pan/Tilt | OFF |  |
|  | NO |  |
| Swap Pan-Tilt | OFF |  |
|  | NO | Change the channel of XY axis (include trimming) |
| Encoder Pan-Tilt | NO | Use encoder correct position |
|  | OFF | Do not use encoder correct position |
| No DMX Signal | KEEP | According to the original state continues to run |
|  | CLEAR | The return of the motor, stop running |
| Display Power Save | NO | Free 30 seconds after closing backlight |
|  | OFF | Backlight ever bright |
| Burn on start up | OFF | Power on directly after reset, no light bulb (need to use the menu or control table to manual light bubble) |
|  | NO | After power on automatic light bubble, must wait for the light bulb light up success can be reset |
| Load Default |  | Press ok key see the confirmation dialog box, again press ok key, Press OK key into edit |

2.3.  Information interface

| Option | Instruction |
| --- | --- |
| Total using time | Cumulative using time (Accuracy to the minute) |
| The use of time | Use of time since the boot (Accuracy to the minute) |
| System error logs | If the red indicator shine ,that mean the lamps runs error . The details can be entered sub-interface to view |
| After you finish view, | you can press the "OK" key to make the error log empty. Pay attention: Sometimes not the Hall or optical coupler installation problems, But the motor cable is connected backwards |

2.4. Manual control interface

This interface use to control present light, neither belong to the from the machine state (didn’t received DMX signal), nor belong to Host state( send DMX signal).

| Option | Instruction |
| --- | --- |
| Reset | Press ok key see the confirmation dialog box, again press ok key, enter the reset interface, all motor reset. |
| Color wheel | 0-255 | Press OK key into edit state, its selected hundred. Press up or down,change channel value .Press again OK key, selected ten editor. Press again OK key, select the edit. Press it again to exit the edit state. |
| …… | 0-255 |  |
| the speed of gobo wheel | 0-255 |  |
| Blub control | ON |  |
|  | OFF |  |

2.5 Advanced interface
Password is “Up down up down “ . For the runner , password is “Left right left right”
Touch operation : Press one time on the “up” key (Appear the first “*” ),Then press one time on the “down” key (Appear the second “*” ) , Press one time on the “up” key again (Appear the third “*” ) , Press one time on the “down” key again (Appear the fourth “*” ) . At last press “OK” key to do the password authentication .
Runner operation : Turn to the left 1 bar (Appear the first “*” ), then turn to the right 1 bar (Appear the second “*” ), Turn to the left 1 bar again (Appear the third “*” ), Turn

to the right 1 bar again (Appear the fourth “*” ) . At last press runner key to do the password authentication.

| Option | Instruction |
| --- | --- |
| Touch screen adjustment | After entering the calibration interface, Follow the cross cursor tips go touch the corresponding position. If the four locations to the correct data is received. Then complete the calibration and save the calibration data. If the calibration fails , This process will continue the cycle ,then can at any time by pressing the "OK" button to interrupt calibration. |
| Reset calibration (Zero calibration) | After entering the sub-interface, Can be adjusted x-axis, Y-axis to the motor’s reset position. To compensate for hardware installation error. With address code and channel value different , reset calibration not support One-digit Two-digit Three-digit edited respectively. Not support long press too . And must be in 1 unit step-by-step calibration . Pay attention : Don’t reset calibration when the motor work. If motor is working ,Please stop it then start to reset calibration.If necessary, Please reset operation one time before reset calibration . |

4.0. Channel Sheet

| Channel | Channel Mode |
| --- | --- |
|  | 19 |  |
| 1 | X |  |
| 2 | X fine adjustment |  |
| 3 | Y |  |
| 4 | Y fine adjustment |  |
| 5 | XY speed |  |
| 6 | dimmer |  |
| 7 | Blackout/Strobe |  |
| 8 | Color wheel |  |
| 9 | Metal pattern gobo |  |
| 10 | Metal pattern effect gobo |  |
| 11 | Glass gobo |  |
| 12 | Glass gobo turning |  |
| 13 | Prism 1 |  |
| 14 | Prisim 1 turning |  |
| 15 | Prism 2 |  |
| 16 | Prism 2 turning |  |
| 17 | Wash |  |
| 18 | Focus |  |
| 19 | Reset | 100－105 blackout 200－205 lamp open 240－255 resent |