LED Spots light

Please read the User menu carefully before using

1.Notice

- Working environment temperature must lower than 40℃ when fixture working

- Do not touch the fixture when operation,since the temperature will getting higher when operation

- Clean and maintenance regularly

- Stop operation fixture immediately when there is something wrong

- Open or Repair fixture by Professional ONLY

- Fixture feature and technical parameter

Voltage：110-240V 50/60HZ

Power：250W

Life-span：50,000H

Color temperature：3200K、5600K

Ra：Ra≥95

Dimmer：0-100％ Linear Dimmer

Control mode：DMX512,manual control,Master&Slave control

Channel:2CH(Dimmer,Strobe)

Working Environment:Apply for Studio,Meeting room,Function hall,hall

Cooling mode：Light housing+Fan

Color：Black

Housing material：Alu

Weight：5KG

Size：430*280*290mm

3.Control panel

4.Display

1.Manual mode

Press Key (ENTER) to Enter manual mode in (Stat)Menu,Press key (Up)or (Down) to select the brightness in <W000>,and <W255> is the Most brightness state of fixture.

Press key (Up)or (Down) to select the speed of strobe in<ST00>,and <st00> is the fastest strobe speed.

- Auto mode

Press (ENTER) to enter Auto mode in (SAUTO) Menu,And select the right auto mode by press Key (UP) or (DOWN)>.From <AT00> to <AT10> are all the build-in program,and from<PR01> to <PR09> are the self-organizing program,this fixture can save 9 self-organizing program.

3.Sound control mode

Enter sound control mode by press (ENTER) under<SOUD>Menu,and select the right Auto mode by press key <UP><DOWN>,and <MOD0> is the “Normal on”mode,and <MOD1>is the “Normal off”mode.can controlled by<SA> and <SP>,<SA>is the build-in effect,and <SP>is self-organizing effect.

4. DMX Controller mode

Press key”ENTER”to enter”DMX controller mode”under<ADDR>Menu,then select the DMX address code by press key <UP> or <DOWN>,The minimum address code is <D001>,and the Maximum is <D255>.and after selected,fixture can controlled by controller.

- Overheat protect

Enter “Overheat protect”by press “ENTER”under <TEMP>Menu,<CURR> is the present temperature.<TOP>is the modify protect temperature value,and “85” is the fixture factory setting,and we suggest NOT to do any change.

- Screen saver

Enter “Protect saver”setting by press “ENTER”under <KEY>Menu,<OFF> Means screen saver off,and “ON” means screen saver is ON. the present temperature.When “Screen saver”On,and fixture without any operation over 20seconds,screen will auto OFF开

- Other select

Master&Slave mode:The Master light setting to Manual mode,and slave light select to address code mode,then can control whole fixture effect by Master light.

※本Fixture have data power-off protection function,so after parameter select&saved,have to waiting for 20S to off fixture,or all of the select will not save.

5.Fixture installing

6.DMX512 connect

7.Channel function