PN：DG-HH05-500-808

PN：DG-HH03-300-808

500W , 300W QCW 808nm

Macro-channel Design Diode Laser Stack

| Version | Change Items | Released Date |
| --- | --- | --- |
| Rev 1 | Initial | 2019.12.01 |

| 光学参数/ Optical Parameters | 单位/Unite | 典型值/Typical |
| --- | --- | --- |
|  |  | DG-HH05-500-808 | DG-HH03-300-808 |
| 输出峰值功率/Output Peak Power | W | 500 | 300 |
| Bar条数量/ Number of Bars | - | 5 | 3 |
| 发光区尺寸/ Emitting Area | mm | 10 X 13.5 | 10 X 6.8 |
| 中心波长11/Center Wavelength 11 | nm | 808 |
| 中心波长公差/Center Wavelength Tolerance | nm | ±10 |
| 快轴90%能量发散角/F-Axis Divergence Angle | ° | 70 |
| 慢轴90%能量发散角/S-Axis Divergence Angle | ° | 12 |
| 偏振模式/Polarization Mode | - | TE |
| 电学性能/Electrical Parameters |  |  |
| 电光转换效率/Conversion Efficiency | % | ≥50 |
| 阈值电流/Threshold Current | A | ≤20 |
| 工作电流/Operating Current | A | ≤100 |
| 工作电压/Operation Voltage | V | ≤10 | ≤6 |
| 热学性能/Thermal Parameters |  |  |
| 工作温度2/Operating Temperature Range2 | ℃ | 20 to 30 |
| 存储温度/Storage Temperature Range | ℃ | -40 to 75 |
| 温漂系数/Wavelength Temperature Coefficient | nm/℃ | ~0.3 |
| 工作条件3/Operation Condition3 |  |  |
| 最大宽度/ Maximum Pulse Width | ms | 400 |
| 占空比/ Duty Cycle | % | 40 |
| 冷却水流量/ Flow Rate | L/min | 4.5 |
| 冷却水要求/ Cooling Water | - | 蒸馏水/DI water |
| 水压/ Cooling Pressure | Mpa | 0.5 |
| 过滤器规格/ Filter | um | 20 |

1  在热沉25摄氏度下测得。Tested at 25℃ cooling tempura.

2  在不结露条件下使用和存储。No-condensing required for operation and storage.

3  超规格使用会导致激光器寿下降。Reduced lifetime if used above nominal operating condition.

| DG-HH05-500-808/ DG-HH03-300-808 |
| --- |
| Peak Power per Bar (W ) | 100 | 80 | 60 |
| Operation Current (A) | 100 | 80 | 65 |
| Pulse width (ms) | Max. Frequency (Hz) |
| 10 | 30 | 40 | 40 |
| 20 | 10 | 15 | 20 |
| 30 | 6 | 10 | 13 |
| 40 | 5 | 8 | 10 |
| 50 | 4 | 6 | 8 |
| 60 | 3 | 5 | 6 |
| 80 | 2 | 4 | 5 |
| 100 | 1 | 2 | 4 |
| 200 |  | 1 | 2 |
| 400 |  |  | 1 |

使用说明 Application Notes:

- 叠阵输出激光会伤眼睛，使用时须遵守IEC四级激光标准安全规范，避免激光直接或间接照射眼睛；

The laser beam could hurt eyes, please follow the standard safety procedures for IEC Class 4 lasers, avoid eyes exposure to radiation.

- 静电击穿导致半导体激光器失效，激光器安装人员须经过培训，操作时须佩戴防静电手腕带，工作台需接地；在供电连接头与激光器连接前，正负极应处于短接状态；

ESD cause diode laser failure, The operator should be trained, wearing ESD grounding straps and the work surface should be grounded. The positive and negative poles shall be connected before the power supply is connected with the laser.

- 电流过冲可能损坏激光器，驱动电源须稳定无过冲。

The current overshoot may damage the laser, and the driving power must be stable without overshoot,

# Text boxes

主要特性 Key Features:                                    应用领域 Application:

- 金锡焊料封装 / AuSn packaging                         ●  美容脱毛/ Hair removal

- 高可靠性 / High reliability

- 长脉宽/ Long pulse-width operation

工作条件/ Operation Condition

外形尺寸/ Dimension